## Slide 1
Plasma Activated Water: A Technology for Acid Generation and Space Crop Production
Dr. Ryan Gott, Dr. Kenneth Engeling, Misle Tessema, Dr. Christina Johnson, Dr. Joel Olson, Bruce Link, Dr. Carolina Franco, Jason Fischer
52nd International Conference on Environmental Systems
Calgary, Canada
July 17th, 2023

## Slide 2: Plasma Activated Water
Introduction of many species
  Oxygen species
    O3, O*, O-, O2+, O2*, O
  Nitrogen species
    N2+, NO, NO2-, NO3-, NH3, NH4, N2*, N
  Water species
    OH, H2O2, H3O+, H2O+, OH*, e-
Use of air as feed gas favors acid production
  NO3- and NO2- have reactions in water that result in HNO3
Zhou, et al. 2020

## Slide 3: Space Infusion Goals
Moon to Mars architecture requires in-situ resource utilization and reuse of materials
Plant growth is of great interest
  Hydroponic pH balancing
  Nutrient solutions
Sanitization is essential
Plasma generated acid has the ability to address all of this and more in a unified system
3

## Slide 4: Setup
Vent
3D Printed Tee
3D Printed Beaker Lid
Beaker
Electrode at Tube Exit
Spill Bucket
Plasma
Gas Inlet Tube
Electrode
Quartz Tube
Air plasma

## Slide 5: pH Results
Chart: DC DI pH
| 0 | 1 | 5 | 10 | 15
He | 5.26 | 5.57 | 5.72 | 5.34 | 4.94
CO2 | 5.26 | 4.25 | 5.08 | 4.75 | 5.28
Ar | 5.26 | 5.82 | 5.59 | 5.29 | 5.01
Air | 5.26 | 3.61 | 3.21 | 2.99 | 2.88
N2 | 5.26 | 3.99 | 3.52 | 3.31 | 3.38
Chart: 400 ns, Pulsed DI
| 0 | 1 | 5 | 10 | 15
He | 5.26 | 5.39 | 4.73 | 4.35 | 5.15
CO2 | 5.26 | 4.08 | 3.94 | 3.98 | 3.84
Ar | 5.26 | 5.24 | 4.3 | 4.25 | 5.47
Air | 5.26 | 4.98 | 4.22 | 3.98 | 3.34
N2 | 5.26 | 4.78 | 4.5 | 4.24 | 3.71
pH Range
  2.7-6.14 (Platinum electrodes)
    Electrode material pH range (2.7-9.7)
  DC/pulsed able to achieve lowest pH
  AC supply limited 4-6.1 range
Conductivity range
  ≈ 0-673 µS·cm-1
  DC full range
  AC/Pulsed ≈ 0-240 µS·cm-1 range

## Slide 6: Nitrate Results
Chart: DC
| 0 | 1 | 5 | 10 | 15
Air | 0 | 26.458 | 93.23 | 120.21 | 128.48
N2 | 0 | 4.8338 | 46.126 | 70.425 | 71.775
DC vs. AC vs. Pulsed
  DC supply up to 126 ppm in 15 minutes
  AC 5-6 ppm at 15 minutes
  400 ns, up to 26 ppm at 15 minutes
Florikan® comparison
  Slow-release ceramic
  Nitrate production comparable for 60/90 day release formula
DC N2 also produces NO2- and NH4+
  On-demand production
  No resupply needed
  Enables microgreen growth on ISS
  Tailor to plan needs as needed
    Adjustments during growth cycle
Chart: Pulsed 400 ns
| 0 | 1 | 5 | 10 | 15
Air | 0 | 1.931 | 3.5544 | 4.7276 | 26.324
N2 | 0 | 0.2368 | 1.448 | 2.501 | 9.9516

## Slide 7: Microgreen Growth Trial
Hoagland’s
DI
PAW pH ≈3
1st PAW Microgreen growth set
PAW pH ≈9
PAW pH ≈7
Hoagland’s
2nd PAW Microgreen growth set
a)
b)
1st PAW Microgreen growth set
  DC air plasma, DI, 15 min. pH≈3
  NO3 ≈ 120 ppm (high)
  Stressed compared to Hoagland's
  Comparable to DI
2nd PAW Microgreen growth set
  Pulsed, DI, 15 min., pH balanced, pH≈6.8 and 9.5
  NO3≈ 25 ppm (Florikan® levels)
  Earlier emergence
  Comparable dry mass to Hoagland’s

## Slide 8: Microgreen Growth Trial

## Slide 9: Sanitization Applications
Biofilm mitigation efforts
  Difficult to remediate
  Common on Space systems
P. aeruginosa
  > 5 log reduction
  Greater than det. Limit

## Slide 10: Martian Applications
Martian atmosphere composition:
95% CO2, 3% N2, 2% Argon
Simulated mixture produced 24.8 ppm on nitrates with DC
  Run for 15 minutes at 1 atm. pressure
Allows for in-situ acid production
Potential for Martian farming
10

## Slide 11: Summary
Plasma generation of acid has numerous ISRU applications
Plant growth and sanitization can both benefit from plasma acid
Why Plasma?
  On-demand production
  No resupply needed
  Power efficiencies will be achieved soon

## Slide 12: Thank you!
Any questions are welcome.
Contact: ryan.p.gott@nasa.gov